## Slide 1
FPGA-ACCELERATED EDGE AI
SUNRISE: Edge AI for Real-Time Solar Energy Nowcasting
A Deep Learning-Based Approach for Real-Time Solar Energy Estimation
using Computer Vision and AMD Kria KV260 FPGA Acceleration
Edge AI
Computer Vision
Deep Learning
FPGA
Vitis AI
AMD/Xilinx
M. Daniel González · Research Project · SUNRISE
Universidad de Oviedo

## Slide 2
AGENDA
Presentation Outline
1
Motivation & Problem Statement
Cloud impact on solar energy and limitations of current approaches
2
Why Edge AI?
CPU vs GPU vs FPGA comparison for deep learning inference
3
Kria KV260 Platform
Heterogeneous architecture: Processing System and Programmable Logic
4
Deep Learning Processing Unit
DPU architecture and hardware-accelerated neural network execution
5
Vitis AI Workflow
End-to-end deployment pipeline: training to runtime inference
6
Platform Preparation
Engineering challenges during KV260 development environment setup
7
DDUNet Adaptation
Model modifications required for FPGA and DPU compatibility
8
Quantization Strategies
Post-Training Quantization vs Quantization-Aware Training
9
Compilation & Results
Performance evaluation: accuracy, speed, and power consumption
10
Future Work
Roadmap toward full solar irradiance prediction system
11
Conclusions
Key achievements and impact of this research
Total duration: ~12 minutes · Q&A session after presentation

## Slide 3
MOTIVATION & PROBLEM STATEMENT
Why Accurate Solar Energy Prediction Matters
The Challenge
☁️
Cloud coverage is the primary factor affecting photovoltaic generation
⚡
Solar power can drop within seconds under heavy cloud cover
Grid instability requires accurate short-term production forecasts
Meteorological sensors are expensive and require regular maintenance
Local microclimates make general weather models unreliable
Impact of Clouds on Solar Generation
Clear sky
Light clouds
Heavy clouds
Overcast
Key Insight
Real-time cloud assessment enables accurate solar energy forecasting without expensive hardware
Our Solution:
A low-cost camera + FPGA-accelerated AI to estimate irradiance from sky images in real time — no meteorological sensors required.
<number>

## Slide 4
WHY EDGE AI?
Deploying Deep Learning on the Edge
CPU
General-Purpose Processor
Sequential execution
Limited parallelism
High latency for CNNs
Not designed for DL inference
Power: ~15-65W
Ideal for: control logic
GPU
Graphics Processing Unit
Massive parallelism
High throughput
High power consumption
Bulkier form factor
Power: ~150-400W
Ideal for: training clusters
FPGA
Field-Programmable Gate Array
Reconfigurable hardware
Custom data paths
Low latency, deterministic
Low power consumption
Power: ~5-20W
Ideal for: Edge AI inference
FPGAs offer the best balance of performance, power efficiency, and flexibility for real-time Edge AI inference
<number>

## Slide 5
HARDWARE PLATFORM
AMD Kria KV260 Vision AI Starter Kit
<number>

## Slide 6
HARDWARE PLATFORM
AMD Kria KV260 Vision AI Starter Kit
Processing System (PS)
ARM Cortex-A53
Quad-core, 1.5 GHz
DDR4 Memory
4 GB, 64-bit
Peripherals
USB, Ethernet, DisplayPort
⏱️
Real-Time Unit
RPU for control tasks
AXI Bus
Programmable Logic (PL)
FPGA Fabric
Custom hardware logic
DPU IP Core
Deep Learning Processing Unit
Video Pipeline
MIPI, ISP, HDMI
⚡
Custom Accelerators
User-defined RTL/IP
💡
The KV260 is designed for Smart Vision and AI applications. The PS handles control and data movement while the PL provides purpose-built hardware acceleration.
<number>

## Slide 7
DEEP LEARNING PROCESSING UNIT
Understanding the DPU Architecture
What is a DPU?
The DPU is a specialized IP core implemented in the FPGA logic designed specifically for neural network inference acceleration.
DPU Inside the FPGA
CPU vs DPU Execution
🖥️ CPU Execution
1. Load instruction from memory
2. Decode instruction
3. Fetch data from memory
4. Execute ALU operation
5. Write result back
→ Sequential, one at a time
🧠 DPU Execution
1. Load input feature map
2. Stream through hardware pipeline
3. Parallel operations
4. Accumulate in dedicated registers
5. Activate & store output
→ 10-100× faster than CPU
Key characteristics:
▪ Convolution engine with pipelining ▪ Parallel MAC operations ▪ Layer-by-layer processing ▪ Fixed-point integer arithmetic ▪ Configurable architecture size
Implemented as a soft IP core inside the FPGA fabric via Vitis AI
<number>

## Slide 8
PLATFORM PREPARATION
Engineering the KV260 Development Environment
1
Initial Setup
Board initialization and firmware verification Out-of-box experience
2
Firmware Update
Latest AMD firmware flashing and bootloader configuration
3
Ubuntu Migration
Decision: Ubuntu 22.04 Stock Ubuntu vs Canonical LTS support assessment
4
USB Detection
Driver configuration Peripheral enumeration Power distribution fix
5
Power Issues
Current budget analysis External power source Stability testing
Engineering Perspective
Platform setup proved non-trivial: documentation gaps, peripheral detection issues, and power delivery constraints required systematic debugging. These challenges are typical when working with cutting-edge embedded AI platforms and provided valuable hands-on experience.
<number>

## Slide 9
VITIS AI DEPLOYMENT WORKFLOW
From PyTorch Model to FPGA Inference
1
Model Training
PyTorch / TensorFlow Train DDUNet for cloud segmentation
2
Quantization
PTQ or QAT Reduce precision to INT8 for efficiency
3
Compilation
Vitis AI Compiler Generate .xmodel for DPU target
4
Deployment
Load .xmodel onto KV260 Initialize DPU
5
Runtime Inference
Capture images Run inference Get predictions
Key Output: .xmodel file
Floating-Point Model (.pth)
Calibration Dataset
Quantized Model (INT8)
DPU Compiler (vai_c_xir)
.xmodel File
<number>

## Slide 10
MODEL ADAPTATION
DDUNet Architecture for Cloud Segmentation for FPGA Deployment
Original DDUNet Architecture
•
Double U-Net with skip connections
✅
Standard convolution layers
✅
ReLU activations
✅
Batch normalization
✅
Max-pooling + upsampling
❌
Operations not in DPU op list
❌
Custom/Variable padding
⚠️
Excessive depth channels
Adapt
FPGA-Optimized Version
✅
Layer compatibility analysis
❌
Replaced unsupported operations
⚠️
Adjusted padding for DPU constraints
✅
Verified DPU op list compliance
✅
Channel dimension optimization
✅
Stride handling configuration
⚠️
Reduced model depth where possible
✅
Validated with Vitis AI analyzer
💡
The DDUNet architecture required significant adaptation — not all layers are supported by the DPU. Unsupported operations were replaced or refactored to ensure compatibility.
<number>

## Slide 11
MODEL ADAPTATION
DDUNet Architecture for Cloud Segmentation for FPGA Deployment
Result
FPGA-Optimized Version
✅
Layer compatibility analysis
❌
Replaced unsupported operations
⚠️
Adjusted padding for DPU constraints
✅
Verified DPU op list compliance
✅
Channel dimension optimization
✅
Stride handling configuration
⚠️
Reduced model depth where possible
✅
Validated with Vitis AI analyzer
💡
The DDUNet architecture required significant adaptation — not all layers are supported by the DPU. Unsupported operations were replaced or refactored to ensure compatibility.
<number>

## Slide 12
QUANTIZATION STRATEGIES
Post-Training Quantization vs Quantization-Aware Training
Post-Training Quantization (PTQ)
Concept
Convert FP32 weights to INT8 after training is complete
Process
1. Load trained FP32 model 2. Run calibration with sample data 3. Quantize weights & activations
Advantages
✅ Fast — no retraining required ✅ Simple workflow ✅ Good starting point
Trade-offs
⚠️ Potential accuracy loss (2-5%) ⚠️ Sensitive to distribution shifts
When to use
When accuracy loss is acceptable or as a baseline comparison
Quantization-Aware Training (QAT)
Concept
Simulate quantization effects during training to recover accuracy
Process
1. Start from trained FP32 model 2. Insert fake quantization nodes 3. Fine-tune with quantization simulation
Advantages
✅ Higher accuracy retention ✅ Better handling of outliers ✅ Robust to calibration data
Trade-offs
⚠️ Requires retraining (longer) ⚠️ More complex pipeline ⚠️ Needs original training setup
When to use
When accuracy is critical or PTQ results are unsatisfactory
☑
Both strategies are evaluated to determine the optimal balance between inference speed, FPGA resource utilization, and prediction accuracy for the cloud segmentation task.
<number>

## Slide 13
MODEL COMPILATION & RESULTS
From .xmodel Generation to Performance Evaluation
Compilation Pipeline
Quantized Model
XIR Graph Representation
DPU Compiler vai_c_xir
.xmodel File
KV260 Runtime
Performance Results
Metric
FP32 (Baseline)
PTQ (INT8)
QAT (INT8)
Accuracy (IoU)
93.2%
90.2%
91.8%
Relative error coverage
-
~ 6.83%
~ 1.09%
Model Size
24.7 MB
6.4 MB
6.4 MB
Inference Time*
127 ms (CPU)
42 ms (DPU)
42 ms (DPU)
Speedup vs CPU
1×
3×
3×
Power Estimate
~15W (CPU)
~8W (KV260)
~8W (KV260)
* Inference time measured on AMD Kria KV260 with DPU (B512 architecture)
Key Observations
▸ QAT recovers ~1.5% IoU over PTQ
▸ 4× model size reduction via INT8
▸ 3× faster inference on DPU vs CPU
▸ FPGA power consumption < 10W
▸ Real-time inference achievable
<number>

## Slide 14
FUTURE WORK
Roadmap Toward Solar Irradiance Prediction
●
Q1: Camera Integration
MIPI camera interface on KV260
Real-time image acquisition driver
Frame buffer optimization
●
Q2: Irradiance Model
Correlation: cloud coverage → irradiance
Train regression model on sky images
Validate against pyranometer ground truth
●
Q3: End-to-End System
Full pipeline: camera → DPU → prediction
Dashboard for real-time visualization
Power generation estimation module
●
Q4: Optimization
Model pruning & further quantization
Multi-location validation
Performance benchmarking & publication
Ultimate Goal →
A complete FPGA-accelerated edge AI system that estimates solar irradiance and predicts photovoltaic energy generation using only a camera as input.
<number>

## Slide 15
CONCLUSIONS
What We Achieved
01
Cloud Segmentation on FPGA
Successfully deployed a DDUNet model for cloud segmentation on the AMD Kria KV260 platform
02
Vitis AI Ecosystem Mastery
Full workflow understanding: Training → Quantization → Compilation → Deployment
03
PTQ vs QAT Evaluation
Systematic comparison of quantization strategies with quantified accuracy impact
04
Platform Foundation
Established the hardware and software infrastructure for future irradiance prediction
This project lays the technological foundation for an FPGA-accelerated Edge AI system
capable of estimating solar irradiance and photovoltaic energy production using only visual information.
<number>